1.0	All countertops on wood or plastic laminate casework shall be constructed of a sold surface material if the countertop has a sink or if wet work is performed on or around the countertop.

2.0	All solid surface material shall have a minimum thickness of 3/4 inch.

3.0	Sinks may be constructed of similar material or may be drop-in stainless steel.  Stainless steel sinks are required in work areas and high traffic use areas where solid surface material sinks may be damaged from use.  Solid surface sinks are acceptable in restrooms.

4.0	Solid surface material backsplash shall be installed on all solid surface material countertops.  A backsplash shall be installed at the end of all solid surface material countertops if the countertop terminates at a wall or against other casework.