1.0	All hinges shall be five knuckle with ball bearings.  All hinges shall have fully concealed bearing and self-lubricating sleeves.

2.0	Door up to 42 inches in width shall use three 4 1/2 inch hinges.  Doors over 42 inches in width shall have three 5 inch hinges.  Doors 90 inches and taller shall use a minimum of 4 hinges.

3.0	All Exterior doors that swing out shall have non-removable pins.

4.0	All hinges on exterior door shall have hinges constructed of solid bronze with the specified plated finish.   All interior door hinges shall be steel with the specified plated finish.

5.0	Suggested manufacturers, but not limited to:

-Hager Companies

-McKinney Products Company

-Mont-Hard Corporation

-Sargent Manufacturing

-Stanley